## Slide 1
LECTURE 5

## Slide 2
AC GENERATOR
A device changing Mechanical energy into Electrical energy.
WORKING PRINCIPLE :
Works on the principle of ELECTROMAGNETIC INDUCTION.

## Slide 3
S
N
G
B1
A
D
B
C
B2
Slip rings
Iron core
Armature coil
Axle
Armature coil
Strong magnet
Slip rings
R1
R1
Brushes
Armature, strong magnets and brushes are the same as used for electric motors.
Slip rings : The two ends of the armature coil are connected to two brass slit rings R1 and R2. These rings rotate along with the armature coil
The main components of AC generator are
- CONSTRUCTION
AC GENERATOR

## Slide 4
Drawing of AC generator
N
S
20
10
0
10
20
G
C
D
A
B
B1
B2
R2
R1
Carbon
brushes
Axle
Conducting
ring
Magnetic field

## Slide 5
AC generator
- Working of the AC generator:
Armature coil ABCD rotates in the magnetic
It cuts the magnetic lines of forces
Produces induced current in the coil
The direction of induced current is determined by the fleming’s right hand rule
Current flows through brush B1 in one direction in the first half of the revolution and through brush B2 in the next half revolution
In the reverse direction, this process is repeated.
Therefore, the induced current produced is of alternating nature.
Such a current is called as alternating current.

## Slide 6
1. The armature coil is rotated in a magnetic field
2. It cuts the magnetic lines of force
3. A current is induced in the armature coil
4. The direction of induced current can be found using Flemings right hand rule
5. In the first half cycle, current flows from brush B1 to B2
6. In the next half cycle, current flows from brush B2 to B1
7. Such a current changes its direction periodically
8. The current produced is called Alternating current
9. Hence, this generator is called an AC generator

## Slide 7
N
N
S
S
DC GENERATOR
NORTH POLE
SOUTH POLE
BRUSHES
ARMATURE
COMMUTATOR
GALVANOMETER
G
30
20
10
0
10
20
30
MAGNETIC FIELD
(DYNAMO)
Where is the dynamo used?

## Slide 9
N
N
S
S
DC GENERATOR
G
30
20
10
0
10
20
30
In DC generator, the flow of current in the circuit is in the same Direction as long as the coil rotates in the magnetic field
This is because one brush is always in contact with the arm of the armature moving up and other brush is in contract with the arm of the armature moving downward in the magnetic field.

## Slide 10
Armature coil
Strong magnet
Split rings or commutator
Brushes
The main components of DC generator are
Bulb
S
N
A
B
C
D
B1
B2
The components such as armature coil, strong magnet, brushes are the same which are used for AC generators.
Split rings or commutator is the same as used in electric motor.
Bulb: The output is shown by the glowing bulb connected across the carbon brushes.
Iron core
Armature coil
Axle
Split ring
- CONSTRUCTION
DC GENERATOR

## Slide 11
Q.
Choose the correct option:
A rectangular coil of copper wires is rotated in a magnetic field. The direction of the induced current changes once in each
two revolutions (b) one revolution
(c) half revolution (d) one-fourth revolution
Ans.
The correct option is (c)

## Slide 12
Thank You