## Slide 1
LECTURE 10

## Slide 2
Electric Meter
Electric power is the rate at which electric energy is dissipated or consumed in an electric circuit
=
work
time
Power
Electric power
=
Energy consumed
time
Energy consumed
=
time
Power

Unit of electric
energy
=
second
watt

kWh
What is kWh
Energy consumed in bigger units
=
h
kW

1
1
1 Unit
Relation between Commercial & S.I. unit of work
1kW h
=
1000 W  3600 s
=
36  105 W - S
1kW h
kW h
=
36  105 joule
1
1kW h = 3.6 × 106 J

## Slide 3
numerical
Type - E
Electric Power
=
Note : Electric power should be in kilowatts & time should be in hours

## Slide 4
An electric refrigerator rated 400 W operates 8 hour/day. What is the cost of the energy to operate it for 30 days at Rs 3.00 per kWh?
1
Given :
Power (P) = 400 W
400
1000
kW
=
0.4 kW
To find :
Time (t) = 30 × 8h = 240 h
Cost per kWh = Rs 3
Formulae :
Solution :
Energy consumed
=
P
×
t
Energy consumed = ?
Energy consumed
= P
×
t
Energy consumed
=
0.4 kW
×
240 h
Cost of energy
=
96
×
3
Cost of energy = Rs. 288
Energy consumed = 96
kWh
=
Ans :
The cost of energy to operate the refrigerator for 30 days is Rs. 288

## Slide 5
An electric heater rated 1000W / 220V operates 2 hours daily. Calculate the cost of energy to operates for 30 days at Rs. 3 per kWh.
2
Power (P)
=
Energy consumed
1000W
Cost of energy to operate for 30 days = ?
=
Energy consumed by electric heater
Time (t)
=
1 kW
2 h/day
P  t
=
=
P  t
=
1 kW  2h
=
2 kWh
Cost of energy to operate
=
2  3
=
Rs. 6 per day
Cost of energy to operate for 30 days
=
30  6
=
Rs. 180
Given :
To find :
Formula :
Solution :
Ans :
Cost of energy to operate electric heater for 30 days is Rs. 180

## Slide 6
A 100 watt electric bulb is lighted for 2 hours daily and four 40 watt bulbs are lighted for 4 hours everyday. Calculate the energy consumed.
3
Given :
Power (P1)
= 100 Watt
Power (P2)
= 40 Watt
To find :
Energy consumed in each case?
time (t1)
= 2 hours
Formula :
Energy consumed
=
Power  time
Solution :
time (t2)
= 4 hours
Energy consumed
=
P1 × t1
=
0.1 kW × 2 h
=
0.2kWh
Energy consumed by 100 watt bulb in one day is 0.2kWh
Energy consumed
=
P2 × t2
=
4 × 0.04 kW × 4 h
=
0.64 kWh
4 ×
Energy consumed by four 40 watt bulbs in one day is 0.64kWh
Ans :
100
1000
kW
0.1 kW
=
40
1000
kW
0.04 kW
=
Total Energy consumed
=
0.64
0.2 +
Total Energy consumed is 0.84kWh
=
0.84kWh

## Slide 7
Which uses more energy, a 250 W TV set in 1 hr, or a 1200 W toaster in 10 minutes ?
4
Given :
Power (P1)
= 250 W
Time (t1)
= 1 h
To find :
Energy consumed = ?
Power (P2)
= 1200 W
Formula :
Energy consumed
=
Pt
Solution :
=
P1 × t1
Energy consumed by a 250 W TV set in 1 h
Ans :
Energy consumed by a 250 W TV set in 1 hr is more than the energy consumed by a 1200 W toaster in 10 minutes
=
0.25 kW × 1h
=
0.25 kWh
Time (t2)
= 10 min
h
= 0.167 h
=
P2 × t2
Energy consumed by 1200 W toaster in 10 min
=
1.2 kW × 0.167 h
=
0.2 kWh
250
1000
kW
0.25 kW
1200
1000
kW
1.2 kW
=
=
10
60
=

## Slide 8
5
A household uses the following electric appliances :
Refrigerator of rating 400W for ten hours each day
Two electric fans of rating 80W for 12 hours each day
Six electric tubes of rating 18 W each for 6 hours each days
Calculate the electricity bill of the household for the month of June. If the cost per unit of electric energy is Rs. 5.00 per kwh
Power (P1)
=
Energy consumed
400W
Electricity bill of household = ?
=
Energy consumed by refrigerator
0.4  10
Power (P2)
=
80W
t1
=
10 h/day
t2
=
12 h/day
Power (P3)
=
18W
t3
=
6 h/day
Cost per unit of electric energy
=
Rs. 5.00
P  t
=
P1  t1
=
=
4 kWh
Given :
To find :
Formula :
Solution :
Energy consumed by two electric fans
2  0.08  12
=
2  P2  t2
=
=
1.92 kWh
Energy consumed by six electric tubes
6  0.018  6
=
6  P3  t3
=
=
0.648 kWh
Total electrical energy consumed
=
4 + 1.92 + 0.648
=
6.568 kWh
Total electrical energy consumed in month of June (30 days)
E = 6.568 kWh  30
=
197.04 kWh
 Electricity bill of operation
=
197.04  5
=
Rs. 985.20
Ans :
Electricity bill of household for month of June is Rs. 985.20
0.4 kW;
0.08 kW;
0.018 kW;

## Slide 9
Thank You