## Slide 1
LECTURE 3

## Slide 2
+
–
+
–
+
–
GEORGE SIMON OHM
V
I
V
I
V
I
Length,
Area of cross section,
Temperature and
Material remain constant.
= R (Resistance)
V a I
OHM’S LAW
OHM’S law gives relation between two electric quantities
V = I × R
This is known as Ohm’s law.
Hence, V = IR
Ohms law states that, the current (I) flowing through a metallic conductor is directly proportional to the potential difference (V), across its ends provided its temperature remains the same.
V
I
= Constant

## Slide 3
RESISTANCE
The S.I. unit of RESISTANCE (R) is ohm (W)
If potential difference across two ends of a conductor is one volt and the current through it is 1 ampere, then the resistance of conductor is 1 ohm
ohm
volt
ampere
=
1
1
1
+
-
R =
V
I
The property of the conductor due to which it opposes flow of current is called RESISTANCE
When atoms are more,
Resistance is more
Current is less
When atoms are less,
Resistance is less
Current is more

## Slide 4
Unit of RESISTIVITY (r) :
R a L
R a
\ R a
R =
Length
Area of cross-section
Material
Temperature
Temperature
r-rho
r
\
S. I unit of resistivity is ohm – metre (W – m).
R =
r
\
W
m
m2
R
L
r =
\
A
r =
R
L
\
A
If the door is wider,
more people can enter
resistance is less.
If wire is thicker,
more electrons can flow
as resistance is less
Hence Ra
1
A
FACTORS AFFECTING RESISTANCE

## Slide 5
Practical understanding of resistivity
–
+
B
A
0
10
20
30
40
A
copper wire
Aluminium wire
Glass rod
Rubber
Electric Circuit
1. Resistivity is a specific property of a material.
2. Different materials have different resistivity

## Slide 6
On what factors does the resistance of a conductor depend?
Ans. :
Length
Q.1.
The resistance of a conductor depends on its
Area of cross – section (thickness)
Temperature
Material

## Slide 7
How does the resistance of a wire change when:
(a) Its length is tripled?
(b) Its diameter is tripled?
(c) Its material is changed to one whose resistivity is three time?
R  l
Q.2.
Ans. :
ρ
l
A
(a)
R =
∴ If l is tripled, resistance is also tripled.
R 
(b)
1
A
or
R 
1
d2
pd2
4
∴ A =
pr2
=
∴ If the diameter is tripled Resistance becomes 1/9 times
R  ρ
(c)
∴ If resistivity is tripled,
resistance is also tripled

## Slide 8
Will current flow more easily through a thick wire or a thin wire of the same material, when connected to the same source? Why?
Ans. :
Q.3.
(i) When connected to a same source, current will flow more easily through the thick wire than the thin wire.
(ii) Resistance R 
1
A

## Slide 9
Thank You