## Slide 1
LECTURE 4

## Slide 2
Circuit of television
To make drawing of
circuits easy
Lets learn
Electrical Symbols

## Slide 3
Cell
-
+
Battery
-
+
KEYS / SWITCHES
Plug key
( )
.
Closed
(On)
( )
Open
(Off)
Closed
(On)
Tap key
Open
(Off)
Measuring Instruments
A
+
-
ELECTRICAL SYMBOLS
Resistance
Variable Resistance
Variable known
Resistance
Ammeter
V
+
-
Voltmeter
G
+
-
Galvanometer
Variable known Resistance

## Slide 4
A wire joint
Wire crossing
Electric bulb

## Slide 5
IT’S TEST TIME
Draw the symbols of components required to make the circuit
Cell
Resistance
Battery
Ammeter
–
+
–
+
A
+
–
Variable Resistance (Unknown)
Variable Resistance
(known)
Voltmeter
Galvanometer
Plug key(on)
Tap key (on)
A wire joint
Electric bulb
Plug key(off)
Tap key (off)
Wire crossing
V
+
–
G
+
–
( )
.
( )

## Slide 6
-
+
While connecting cells to each other always connect unlike terminals.
A
+
-
V
+
-
For devices like ammeter or voltmeter, the side from which current enters is positive (+) and the side from current exits is negative (-).
SOME IMPORTANT POINTS TO REMEMBER

## Slide 7
A
( )
+
–
–
+
Ammeter is connected in series with the cell.
+
–
A
( )
+
–
V
A
B
–
+
Voltmeter is connected in parallel with the cell.
As the current in the circuit is not divided
As the current in the circuit is divided
Voltmeter
Ammeter
It has very low resistance
So it allows almost entire current to pass
So it doesn’t disturb the current as well as measures the current
It is made from a material having infinite resistance
So the current it allows is negligible or almost zero
SOME IMPORTANT POINTS TO REMEMBER

## Slide 8
How is a voltmeter connected in the circuit to measure the potential difference between two points?
Ans. :
Q.1.
To measure the potential difference between two points, voltmeter must always be connected in parallel to the points.
What happens if an ammeter is connected in parallel?
Ans. :
Q.2.
If an ammeter is connected in parallel, the resultant resistance of the circuit decreases and more current passes through the ammeter. Hence, the ammeter is likely to be burnt.
What happens if a voltmeter is connected in series?
Ans. :
Q.3.
When the voltmeter is connected is series, the resistance of the circuit becomes high and there is considerable fall in current through the circuit. Thus, the voltmeter will not give the correct reading of the potential difference.

## Slide 9
( )
V
A
-
+
A
V
+
-
+
-
How many mistakes can you find in this diagram

## Slide 10
and = R (Constant)
V a I
Nichrome wire
Length : 3 m
Diameter : 0.02 cm
A
+
–
V
+
–
+
–
No of Cells | I (A) | P.D (V) | 
= R (Ω)
1
2
3
2
1
3
2
4
6
2
2
2
V
I
O
1
2
3
4
2
4
6
8
(2, 1)
(4, 2)
(6, 3)
Linear
Experimental verification of Ohm’s law

## Slide 11
Thank You