## Slide 1
LECTURE 7

## Slide 2
A hot plate of an electric oven connected to a 220 V line has two resistance coils A and B, each of 24 W resistances, which may be used separately, in series, or in parallel. What are the currents in the three cases ?
11
220 V
A
K
I
+
–
R=24W
220 V
A
K
I
+
–
R=24W
A
K
I
+
–
R=24W
220 V
R=24W
R=24W
R=24W
R=24W
I1 = ?
I2 = ?
I3 = ?

## Slide 3
A hot plate of an electric oven connected to a 220 V line has two resistance coils A and B, each of 24 W resistances, which may be used separately, in series, or in parallel. What are the currents in the three cases ?
11
Given :
Voltage (V)
= 220 V
Resistance (R)
= 24 W
To find :
Current when coils are used separately (I1)
= ?
Current of series combination (I2)
= ?
Current of parallel combination (I3)
= ?
Formulae :
V
=
IR
RS
=
R1 + R2
=
+
Solution :
Case I : Coils used separately
According to ohm’s law
V
=
I1R
I1
=
\
=
=
9.166 A
I1
\
Case II : Coils in series
RS
=
R + R
\
RS
=
24 + 24
\
RS
=
48 W
Total resistance in series
According to ohm’s law
V
=
I2RS
I2
=
\
=
=
4.58 A
I2
\
Case III : Coils in parallel
Total resistance in parallel
=
+
\
=
+
=
\
RP
=
\
RP
=
12 W
According to ohm’s law
V
=
I3RP
I3
=
\
=
=
18.33 A
I3
\
Ans :
The currents flowing through the coils when they are used separately, in series and in parallel are 9.166 A, 4.58 A and 18.33 A respectively

## Slide 4
numerical
Type - b
V
=
IR
R
=
ρl
A
(A = r2)

## Slide 5
(a) How much current will an electric bulb draw from a 220 V source, if the resistance of the bulb filament is 1200 Ω ?
(b) How much current will an electric heater coil draw from a 220 V source, if the resistance of the heater coil is 100 Ω ?
+
–
1st circuit
2nd circuit
V1 = 220V
I1 = ?
R1 = 1200 W
V2 = 220V
I2 = ?
R2 = 100 W
+
–
1

## Slide 6
R1 = 1200 Ω,
I1 = ?
V = IR
220
×
1200
I1 = 0.18 A
I1
V1 = 220 V;
R2 = 100 Ω.
V2 = 220 V;
I2 = ?
V1 = I1R1
=
I1
=
220
1200
22
120
=
V2 = I2R2
11
60
220
×
100
I2 = 2.2 A
I2
=
I2
=
220
100
22
10
=
Given :
To find :
Formula:
Solution :
Current through bulb is 0.18 A
Ans :
Current through heater is 2.2 A
\
\
\
\
(a) How much current will an electric bulb draw from a 220 V source, if the resistance of the bulb filament is 1200 Ω ?
(b) How much current will an electric heater coil draw from a 220 V source, if the resistance of the heater coil is 100 Ω ?
1

## Slide 7
The potential difference between the terminals of an electric heater is 60 V when it draws a current of 4 A from the source. What current will the heater draw if the potential difference is increased to 120 V ?
Given :
Potential difference (V)
= 60 V
Current (I)
= 4 A
Increased Potential difference (Vi)
= 120 V
To find :
Current (I)
= ?
Formula :
V =
IR
Solution :
V =
IR
R =

R =

15
1
R =
15 W

When V is increased to 120V then,
I
Vi
R
=
120
15
=
8
1
I =
8 A

‘V’ is increased but ‘R’ remains constant
2
Ans :
The current in the heater is 8 A

## Slide 8
Resistance of a metal wire of length 1 m is 26 Ω at 20°C. If the diameter of the wire is 0.3 mm, what will be the resistivity of the metal at that temperature?
Ans :
(R)
= 26 Ω
(l)
= 1m
(d)
= 0.3 mm
3
l = 1m
d = 0.3mm
R = 26 
∴ r
= 0.15 mm
= 15 x 10-5m
R =
ρ
l
A
∴ ρ =
R x A
l
=
R x r2
l
26 x 3.14 x (15 x 10-5)2
1
=
26 x 3.14 x 225 x 10-6
∴ Resistivity of metal = 1.84 × 10–6 m
ρ =
1.84 x 10-6 Ωm
=

## Slide 9
A wire of given material having length l and area of cross section A has a resistance of 4 Ω. What would be the resistance of another wire of the same material having length l/2 and area of cross section 2A?
Wire
l
A
2A
l/2
4
Ans :
(i)
For 1st wire :
… … … …(i)
= 4 
R1 =
ρ
l
A
∴ The resistance of new wire is 1 
=
(ii)
For 2nd wire :
R2 =
ρ
l / 2
2A
1
4
=
1
4
x R1
… … … [from (i)]
ρ
l
A
=
1
4
x 4
∴ R2 =
1 Ω

## Slide 10
When a 12V battery is connected across an unknown resistor, there is a current of 2.5 mA in the circuit. Find the value of the resistance of the resistor.
Q.5.
Given :
V
= 12 V
Formula :
Solution :
The value of the resistance of the resistor is 4800 Ω
To find :
V
I
I
= 2.5 mA
= 2.5 x 10-3 A
= ?
R
=
R
12V
2.5 x 10-3
=
R
= 4800 Ω

## Slide 11
Let the resistance of an electrical component remains constant while the potential difference across the two ends of the component decrease to half of its former value. What change will occur in the current through it?
Q.6.
Ans :
V = IR
… … … (i)
∴ The current through the component will also become half.
V
R
According to Ohm’s law,
=
Now, the potential difference is reduced to half.
I =
∴
New potential difference V’ =
V
2
… … … (ii)
∴ Resistance remains constant,
New current I’ =
V’
R
New current I’ =
V
2R
[from(ii)]
1
2
x
V
R
I’ =
1
2
I

## Slide 12
(a) Draw a schematic diagram of a circuit consisting of a battery of three cells of 2 V each, a 5 resistor, an 8  resistor, and a 12  resistor and a plug key, all connected in series.
(b) Redraw the above circuit putting an ammeter to measure current through the resistors and a voltmeter to measure potential difference across 12  resistor. What would be the readings in ammeter and voltmeter.
Ans. :
Q.7.
Since all the three resistors are in series,
V
R
=
5
-
+
(
(
8
12
2V
2V
2V
K
(a)
5
-
+
(
(
8
12
2V
2V
2V
K
V
-
+
A
-
+
(b)
Total Resistance R = 5 + 8 + 12
= 25 
∴ Current I =
6
25
= 0.24 A
Across 12 resistor, potential difference
V = IR
= 0.24 x 12
= 2.88 V
∴ Ammeter Reading = 0.24 A
Voltmeter Reading = 2.88 V

## Slide 13
A copper wire of length 2 m and area of cross-section 1.7  10-6 m2 has a resistance of 2  10-2 ohms. Calculate the resistivity of copper
5
Given :
Length (l)
= 2 m
To find :
Resistivity ()
= ?
Formula :
R =
Area (A)
= 1.7  10-6 m2
Resistance (R)
= 2  10-2 
 =
R  A
l
Solution :
R =
 =
2  10-2
2
=
1.7  10-8  m
Ans :
The resistivity of copper is 1.7  10-8  m
l = 2m
A = 1.7  10-6 m2
R = 2  10-2 
 1.7  10-6

## Slide 14
Thank You