## Slide 1
LECTURE 9

## Slide 2
numerical
Type - D
I2Rt
V2t
VIt
W =
W =
W =
joule
joule
joule
R
Formulae based
on work done in joules
Power =
Work done
Time
I2Rt
P =
t
I2R
P =
watt
V2
P =
R
watt
P = VI watt

## Slide 3
100 J of heat is produced each second in a 4 W resistance. Find the potential difference across the resistor.
1
Given :
Heat (H)
= 100 J
Resistance (R)
= 4 Ω
Time (t)
= 1 sec
To find :
P.D. (V) = ?
H = J
Formula :
H =
J
Solution :
H =
J
\
V =
\
V =
\
V =
\
20 V
V =
Ans :
Potential difference across the resistor is 20 V.

## Slide 4
Compute the heat generated while transferring 96000 coulomb of charge in one hour through a potential difference of 50 V.
2
Given :
P.D. (V)
= 50 V
Time (t)
= 1 hr
= 1 × 60 × 60 s
To find :
Heat (H) = ?
Formulae :
I
=
H
=
VIt
Solution :
I
=
\
I
=
1
160
3
80
\
I
=
A
H
=
VIt
\
H
=
50
×
×
60
×
60
1
20
\
H
=
4800000
\
H
=
4.8 × 106 J
Ans :
Heat generated is 4.8 × 106 J
H =
joule
H = joule
H = joule
Charge (Q)
= 96000 C

## Slide 5
An electric iron of resistance 20 W takes a current of 5 A. Calculate the potential difference and heat developed in 30 s.
3
Given :
Current (I)
= 5 A
Time (t)
= 30 s
To find :
Heat (H) = ?
Formulae :
V
=
IR
H
=
VIt
Solution :
V
=
IR
Resistance (R)
= 20 W
\
V
=
5 × 20
\
V
=
100 V
H
=
VIt
\
H
=
100
\
H
=
15000
× 5
× 30
\
H
=
1.5 × 104 J
Ans :
The amount of heat developed in the electric iron is 1.5 × 104 J
H =
joule
H = joule
H = joule
P.D (V) = ?

## Slide 6
An electric iron consumes energy at a rate of 840 W when heating is at the maximum rate and 360 W when the heating is at the minimum. The voltage is 220 V. What is the current in each case?
4
220 V
Imax = ?
K
A
+
–
min
max
Pmax = 840 W
Pmin= 360 W
Imin = ?

## Slide 7
An electric iron consumes energy at a rate of 840 W when heating is at the maximum rate and 360 W when the heating is at the minimum. The voltage is 220 V. What is the current in each case?
4
Given :
Power at maximum rate (Pmax)
= 840 W
Power at minimum rate (Pmin)
= 360 W
Potential Difference (V)
= 220 V
To find :
Imax
= ?
Imin
= ?
Formula :
P
= VI
Solution :
When heating is at the maximum rate: Pmax = 840 W, V = 220 V
Pmax
=
VImax
\
Imax
=
Pmax
V
\
Imax
=
840
220
11
42
\
Imax
=
3.82 A
When heating is at the minimum rate: Pmin = 360 W, V = 220 V
\
Imin
=
360
220
11
18
\
Imin
=
1.64 A
Ans :
Imax = 3.82 A ,
Imin = 1.64 A.
P =
I2R
watt
P = VI watt
P = watt

## Slide 8
An electric bulb is rated 220 V and 100 W. When it is operated on 110 V, the power consumed will be ?
5
A
K
–
+
V
220 V
P1 = 100 W
110 V
P2 = ?

## Slide 9
An electric bulb is rated 220 V and 100 W. When it is operated on 110 V, the power consumed will be ?
5
Given :
Power (P1)
= 100 W
P.D. (V1)
= 220 V
To find :
Power (P2) = ?
Formula :
P
=
Solution :
P1
=
\
100
=
\
R
=
P =
I2R
watt
P = VI watt
P = watt
Ans :
The power consumed at 110 V is 25 W.
P.D. (V2)
= 110 V
\
R
=
484 W
This formula is best suited as P and V are given
Resistance remains constant even at 110 V
\
P2
=
\
P2
=
\
P2
=
\
P2
=
25 W
242
55
121
55
11
5
1
5

## Slide 10
An electric bulb is connected to a 220 V generator. The current is 0.50 A. What is the power of the bulb?
6
A
K
–
+
V
I = 0.5 A
220 V
Power (P) = ?

## Slide 11
An electric bulb is connected to a 220 V generator. The current is 0.50 A. What is the power of the bulb?
6
Given :
Current (I)
= 0.50 A
P.D. (V)
= 220 V
To find :
Power (P) = ?
Formula :
P
= VI
Solution :
P
= VI
\
P
=
220
×
0.50
\
P
=
110 W
P =
I2R
watt
P = VI watt
P = watt
Ans :
Power of the bulb is 110 W.

## Slide 12
An electric heater of resistance 8 W draws 15 A from the service mains for 2 hours. Calculate the rate at which heat is developed in the heater.
7
Given :
Resistance (R)
= 8 W
Current (I)
= 15 A
To find :
Power (P) = ?
Formula :
P
=
I2R
Solution :
P
=
I2R
\
P
=
(15)2 × 8
\
P
=
1800 J/s
Ans :
Heat is produced by the heater at the rate of 1800 J/s

## Slide 13
A
K
+
–
Two lamps, one rated 100 W at 220 V, and the other 60 W at 220 V, are connected in parallel to electric mains supply. What current is drawn from the line if the supply voltage is 220 V ?
8
P2= 60 W
220 V
P1= 100 W
I = ?

## Slide 14
Two lamps, one rated 100 W at 220 V, and the other 60 W at 220 V, are connected in parallel to electric mains supply. What current is drawn from the line if the supply voltage is 220 V ?
8
Given :
Power (P1)
= 100 W
P. D. (V)
= 220 V
To find :
Current (I) = ?
Power (P2)
= 60 W
Formula :
P
=
VI
Solution :
I1
=
P1
=
VI1
\
I1
=
A
\
Current drawn by the bulb of rating 100 W is
I2
=
P2
=
VI2
\
I2
=
A
\
Similarly, Current drawn by the bulb of rating 60 W is
Current drawn from the line
=
+
=
0.727 A
Ans :
Current drawn from the line is 0.727 A
=
I1 + I2

## Slide 15
Two conducting wires of the same material and of equal lengths and equal diameters are first connected in series and then parallel in a circuit across the same potential difference. The ratio of heat produced in series and parallel combination would be : (a) 1:2 (b) 2:1 (c) 1:4 (d) 4:1
Ans. :
1
Rp
=
+
Q.5.
Let Rs be the equivalent resistances of the wire when connected in series and Rp be the equivalent resistance, when connected in parallel.
(c) 1:4
1
R
1
R
=
2
R
∴ Rs = R + R = 2R
1
Rp
=
∴
R
2
H =
V2t
R
Hs
Hp
V2t
Rs
V2t
Rp
=
Rp
Rs
=
∴
Hs
Hp
=
1
4

## Slide 16
Thank You